## Slide 1
This work is performed in the Framework Collaboration Agreement KN3573/GEN between CERN and CEA and its Addendum n°2 KE3800

## Slide 2
Contents
1- Introduction - context
2- HeII heat transport and transfer
3- Heat exchanger design
4- D2 Heat exchanger selection
4- Conclusion

## Slide 3: Example for 5R
Q6
Q5
Q4
D2
LHC
HL-LHC
limit
Criteria for a good heat exchanger :
@ Efficiency : release maximum heat with minimum DT
@ Ability to cope with transient
@ Compactness : minimum dedicated overall volume
@ Reliability
@ Cost
HL-LHC layout

## Slide 4
D2 layout and heat loads

## Slide 5
Example of a pressurized HeII/saturated He heat exchanger :
Here some pipes filled with pressurized liquid are immersed in a saturated bath (a “Tore-Supra” like solution)
A simple (and false) idea consists to believe that increasing the pipe length will systematically improve the heat exchanger efficiency

## Slide 6
« Saturated » HeII channel
Pressurized HeII channel
DT4 large cross section HeII bath, small DT
DT2 due to wall heat transfer (Kapitza+copper)
DT3 inside saturated HeII pipe
DT1 inside pressurized HeII
Tmax at heat exchanger inlet
Tmin at liquid-vapor interface
Liquid
HeII
HeI
Vapor
Temperature
margin
Sub cooling
DP (immersion depth)
C
B
A
Heat exchanger consists in a periodic arrangements of channels in parallel:
let’s consider here only one period
Bath level
DP
(immersion
depth)
DTtot=DT1+DT2(outlet)+DT4=DT2(inlet)+DT3+DT4
A
B
B
A

## Slide 7
DTtot=DT1+DT2(outlet)+DT4=DT2(inlet)+DT3+DT4
Usually the liquid height above the heat exchanger is quite small (as compared to the heat exchanger length) and the cross section for heat flux higher than those allocated for the HeII in channels, so DT4 is almost negligible as compared to the other terms of previous equation.
DTtot ≈ DT1+DT2(outlet) ≈ DT2(inlet)+DT3
Longitudinal DT due to heat transport in HeII (DT1 and DT3) only depends on overall cross section, heat exchanger length and heat amplitude and repartition along the whole heat exchanger length.
Bath level
DP
DT1
DT3
DT2
To optimize DTtot we assume DT1= DT3 and consequently the heat flux is evenly deposited along the heat exchanger so DT2=cte
Inside HeII (DT1 or DT3) the heat transport is given by:

## Slide 8
So longitudinal DT is in the form
L
Bath level
DP
DT1
DT3
DT2
L

## Slide 9
So transverse DT is in the form
Which results in :
This expression has a minimum equal at
for
Which also leads to
DT1 (= DT3) = DT2 !
Bath level
DP
DT1
DT3
DT2

## Slide 10
DT1 (= DT3) = DT2 !
The way step by step to proceed to optimize a HeII/HeII heat exchanger design :
2. Increase the number of pipes while keeping the overall cross section (i.e. decreasing accordingly the pipe diameter) increases the heat transfer area and decrease DT2 while keeping DT1 (and DT3) almost constant : the number of pipes should be increased until pipe diameter becomes to small and space occupied by pipe walls matters too.
3. Calculate the optimum pipe length L to obtain DT3 (or DT1) =DT2
1. Assume an overall cross section for the heat exchanger. Calculate the corresponding overall cross section for the saturated HeII only using DT1 =DT3
Bath level
DP
DT1
DT3
DT2
L

## Slide 11
Application to the future D2 HL-LHC dipole
Design criteria :
W=70W
Tsat =2.K
Ppress =4bar
Tpress max=2.044K
Diameter of the two connecting holes to D2 magnet : 0.136m I.D.
Considering pressure to be sustained by pipes (20bar in case of quench), and minimum thickness/ space access for welding the copper pipes to the end plate, pipes of 12X10mm appears to be the best choice.
Previous relation DT1 = DT3 ( resulting in )
allows to calculate the number of pipes knowing the total cross section
with
gives

## Slide 12
Application to the future D2 HL-LHC dipole (continuing…)
Previous relation DT1 (or DT3) = DT2 allows to calculate the optimal length
A =
with
gives :
1.2m
and
The objective was a maximal DTtot =44mK so there is a lot of margin. It will be used to :
1) To decrease down to 104 the number of pipes to take into account the presence of the inner diameter wall of the two connecting holes
2) To decrease down to 0.5m the pipe length L so the heat exchanger fits in the magnet cryostat
This will results in a transversal DT2 =20mK and a longitudinal DT3=5mK, this latter one being very small, it avoid to need a high level to keep subcooling (only a few cm is enough). This validates the former assumption of DT4 negligible (<1mK)
Using hkap=600T3 and k=6T
And the overall DT

## Slide 13
Conclusion
A procedure to design step by step a HeII/HeII heat exchanger has been described and applied to the future D2 HL-LHC dipole at CERN.
A prototype of this heat exchanger is under construction and will be tested at CEA/SBT during 2019
Thank you for your attention !